## Slide 1: 19 CS 2109
COMPUTER NETWORKS AND SECURITY

## Slide 2: Error Control
Session-9 and 10

## Slide 3: Error Detection and Correction
Types of Errors
Detection
Error Correction

## Slide 4: Error Detection and Correction
Data can be corrupted during transmission. For reliable communication, error must be detected and corrected
Error Detection and Correction are implemented either at the data link layer or the transport layer of the OSI model

## Slide 5: Type of Errors

## Slide 6: Type of Errors(cont’d)
Single-Bit Error
~ is when only one bit in the data unit has changed.

## Slide 7: Type of Errors(cont’d)
Multiple-Bit Error
~ is when two or more nonconsecutive bits in the data unit have changed(ex : ASCII B - ASCII LF)

## Slide 8: Type of Errors(cont’d)
Burst Error
~ means that 2 or more consecutive bits in the data unit have changed

## Slide 9: Detection
Error detection uses the concept of redundancy, which means adding extra bits for detecting errors at the destination

## Slide 10: Detection(cont’d)
Redundancy

## Slide 11: Detection(cont’d)
Detection methods

## Slide 12: Detection(cont’d)
Parity Check
  A parity bit is added to every data unit so that the total number of 1s(including the parity bit) becomes even for even-parity check or odd for odd-parity check
  Simple parity check

## Slide 13: Detection -examples
Example 1
Suppose the sender wants to send the word world.
In ASCII the five characters are coded as
1110111 1101111 1110010 1101100 1100100
The following shows the actual bits sent
11101110 11011110 11100100 11011000 11001001

## Slide 14: Detection -examples
Example 2
Now suppose the word world in Example 1 is received by the receiver without being corrupted in transmission.
11101110 11011110 11100100 11011000 11001001
The receiver counts the 1s in each character and comes up with even numbers (6, 6, 4, 4, 4). The data are accepted.

## Slide 15: Detection -examples
Example 3
Now suppose the word world in Example 1 is corrupted during transmission.
11111110 11011110 11101100 11011000 11001001
The receiver counts the 1s in each character and comes up with even and odd numbers (7, 6, 5, 4, 4). The receiver knows that the data are corrupted, discards them, and asks for retransmission.

## Slide 16: Two –Dimensional Parity Check

## Slide 17: Detection - example
Example 4
Suppose the following block is sent:
10101001 00111001 11011101 11100111 10101010
However, it is hit by a burst noise of length 8, and some bits are corrupted.
10100011 10001001 11011101 11100111 10101010
When the receiver checks the parity bits, some of the bits do not follow the even-parity rule and the whole block is discarded.
10100011 10001001 11011101 11100111 10101010

## Slide 18: Detection(cont’d)
CRC(Cyclic Redundancy Check)
~ is based on binary division.

## Slide 19: Detection(cont’d)
CRC generator
~ uses modular-2
division.
Binary Division
in a
CRC Generator

## Slide 20: Detection(cont’d)
Polynomials
  CRC generator(divisor) is most often represented not as a string of 1s and 0s, but as an algebraic polynomial.

## Slide 21: Detection(cont’d)
A polynomial representing a divisor

## Slide 22: Detection(cont’d)
Standard polynomials

## Slide 23: Detection(cont’d)
Checksum
~ used by the higher layer protocols
~ is based on the concept of redundancy(VRC, LRC, CRC ….)

## Slide 24: Detection(cont’d)
Checksum Generator

## Slide 25: Detection(cont’d)
To create the checksum the sender does the following:
  The unit is divided into K sections, each of n bits.
  Section 1 and 2 are added together using one’s complement.
  Section 3 is added to the result of the previous step.
  Section 4 is added to the result of the previous step.
  The process repeats until section k is added to the result of the previous step.
  The final result is complemented to make the checksum.

## Slide 26: Detection(cont’d)
data unit and checksum

## Slide 27: Detection(cont’d)

## Slide 28: Detection(cont’d)
Example ( at a sender)
Original data : 10101001 00111001
10101001
00111001
--------------
11100010 Sum
00011101 Checksum
10101001 00111001 00011101

## Slide 29: Detection(cont’d)
Example ( at a receiver)
Received data : 10101001 00111001 00011101
10101001
00111001
00011101
---------------
11111111  Sum
00000000  Complement

## Slide 30: Error Correction
Error correction can be handled in two ways
when an error is discovered, the receiver can have the sender retransmit the entire data unit.
a receiver can use an error-correcting code, which automatically corrects certain errors.

## Slide 31: Error Correction(cont’d)
Single-Bit Error Correction
  parity bit
  The secret of error correction is to locate the invalid bit or bits
  For ASCII code, it needs a three-bit redundancy code(000-111)

## Slide 32: Error Correction(cont’d)
Redundancy Bits
~ to calculate the number of redundancy bits (R) required to correct a given number of data bit (M)

## Slide 33: Error Correction(cont’d)
If the total number of bits in a transmittable unit is m+r, then r must be able to indicate at least m+r+1 different states
2r  m + r + 1
ex) For value of m is 7(ASCII), the smallest r value that can satisfy this equation is 4
24  7 + 4 + 1

## Slide 34: Error Correction(cont’d) Relationship between data and redundancy bits

## Slide 35: Error Correction(cont’d)
Hamming Code
~ developed by R.W.Hamming
positions of redundancy bits in Hamming code

## Slide 36: Error Correction(cont’d)
each r bit is the VRC bit for one combination of data bits
  r1 = bits 1, 3, 5, 7, 9, 11
  r2 = bits 2, 3, 6, 7, 10, 11
  r4 = bits 4, 5, 6, 7
  r8 = bits 8, 9, 10, 11

## Slide 37: Error Correction(cont’d) Redundancy bits calculation(cont’d)

## Slide 38: Error Correction(cont’d) Redundancy bits calculation(cont’d)

## Slide 39: Error Correction(cont’d) Calculating the r values

## Slide 40: Error Correction(cont’d) Error Detection and Correction

## Slide 41: Error Correction(cont’d)
Error detection using Hamming Code

## Slide 42: Error Correction(cont’d)
Multiple-Bit Error Correction
  redundancy bits calculated on overlapping sets of data units can also be used to correct multiple-bit errors.
  Ex) to correct double-bit errors, we must take into consideration that two bits can be a combination of any two bits in the entire sequence